Project summary: RoboWay – Inverted Pendulum

André Sünnemann	31.03.2014
IAV4

RoboWay is a self balancing robot on two wheels which is controlled by a little 8 bit microcontroller.

The goal of this project was to learn more about writing efficient C programs, learn how various filter techniques such as the Kalman Filter or the Complementary Filter works, learn how to write programs for AtMega micro controllers in low level C.
Also it was a challenge to to design the pid controller to work fine.

For position control RoboWay uses two sensors, an accelerometer an a gyroscope.
The accelerometer measures the g forces on the x, y and z axis and the gyroscope measures the angular rate in degrees per second.

A Complementary Filter filters out the bad properties like the drift of the gyroscope and the high sensitivity of the accelerometer.
So the Complementary Filter uses a high pass filter for the gyroscope and a low pass filter for the accelerometer.
The summary of these two values is the real angle of RoboWay which is used for the pid controller.

The pid controller uses the current angle calculated by the Complementary Filter and a reference angle for calculating an output value between -255 and +255.
This value is directly proportional to the motor direction and the motor speed, because the two motors are driven by a pwm signal.

In physics RoboWay has its mass on its highest point. So it is an inverted pendulum or a so called unstable system.
Unstable systems are a classic problem in control technology.
There are much solutions like pid controllers, self learning neuronal networks (a.e. Fuzzy Systems) for this problem.
I've used a very simple pid controller, because the little micro controller I've used is not as fast as it should be for self learning neuronal networks.

RoboWays body is made by a 3D printer and the controller board is also selfmade.

Further information available here:
www.edv-peuker.de/roboway

A video is available at YouTube:
www.youtube.com/watch?v=RWkzlugv2Mk